## Slide 1: The model description
This example contains:
CPG (Corner Point Geometry) grid setup
Few grid and rock properties setup:
  mesh generation
  input files (grdecl)
Physics:
  Geothermal
  Deadoil (isothermal)
Well perforation definition:
  using Python code (XYZ and IJK)
  using SCH file (COMPDAT)
Well controls
  BHP
  Rate with BHP constraint
  Cyclic production and injection

## Slide 2: DARTS Model and inheritance
Model_CPG
Model_Geothermal
Model_DeadOil
DARTSModel
A part of open- DARTS package
The model files
Reservoir related code
Physics related code

## Slide 3: Case files
case_base.py
case_40x40x10.py
case_generate_5x3x4.py
Case files
Common setup
Each case can overwrite some properties
A synthetic grid can be generated or can be read from .grdecl files
Defined in case_base.py:
idata.generate_grid = 'generate' in case
Copy everything from the “base” (or your own) case and overwrite only what is needed:
Selecting a case by its name (set_case.py):

## Slide 4: Grid generation
The grid is generated with a function gen_cpg_grid and can be
with a regular layers thickness:
  Defined in case_generate_51x51x1.py:
  geom.nx = 51
  geom.ny = 51
  geom.nz = 1
  geom.dx = 4000. / geom.nx
  geom.dy = geom.dx
  geom.dz = 100. / geom.nz
and the irregular layers thickness:
  Defined in case_generate_5x3x4.py:
  geom.dx = np.array([500, 200, 100, 300, 500])
  geom.dy = np.array([1000, 700, 300])
  geom.dz = np.array([100, 150, 180, 120])

## Slide 5: Model
  Input files in Eclipse format
  (grdecl)
  Results
  Model
  scripts
  Grid
  Keywords: SPECGRID, COORD, ZCORN, ACTNUM
  Rock properties
  Keywords: PORO, PERMX, [PERMY, PERMZ]
  Model folder
  ResInsight
  ParaView
  One file per time step
  Vtk file (3D data)
  grdecl (3D data)
  Initial+final or one file per time step
  Well locations and static data: Perm, Depth, Volume
  Vtk files (3D data)
  Well results
  pkl
  xlsx
  Output folders for each case

## Slide 6: CPG Reservoir
  Read text files with grid and rock properties:
arrays = read_arrays(self.gridfile, self.propfile)
self.reservoir = CPG_Reservoir(self.timer, arrays) self.reservoir.discretize()
  Initialize the mesh (filter inactive cells, allocate arrays, compute connectivity, transmissibility, etc)
Console output:
  One can implement own file reader or fill it in Python code depending on purpose.
  The main input of the reservoir class is a dictionary of numpy arrays containing grid data and rock properties.

## Slide 7: Over- and underburden layers generation
  If that layers were not generated in the geological modeling software, or one uses mesh generation option in open-DARTS, it is possible to do that using the next function:
  Reservoir
  Overburden
  Underburden
  Note: this feature doesn’t work well if the top or the bottom layers are fully or partly inactive (due to ACTNUM=0, PORO=0, thickness=0)

## Slide 8: Over- and underburden rock properties
Defined in case_base.py

## Slide 9: Fault transmissibility multipliers
  CPG_Reservoir class has an option to pass a filename with fault location and multipliers in format:
  I1 J1 K1 I2 J2 K2 M
  where
    I1, J1, K1 - indices of the first cell, integers
    I2, J2, K2 - indices of the second cell, integers
    M - multiplier, float value
  For example, setting M=0.0 will make the fault impermeable.

## Slide 10: Boundary conditions
Defined in case_base.py:
geom.bound_volume = 1e18 # lateral boundary volume, m^3
  Boundary conditions:
  top and bottom – no flow
  lateral boundaries – large volume
  In case ACTNUM array is defined, the volume will be set at the closest active cell:

## Slide 11: Initial conditions (geothermal physics)
Defined in model_geothermal.py:
  Uniform p,T
  Non-uniform p,T
  (set by gradient)
  Water saturation

## Slide 12: Initial conditions (deadoil physics)
  Water saturation
  Pressure
Defined in model_deadoil.py:

## Slide 13: Well perforations
Screen output (if verbose)
  Well index
Adding wells and perforation is performed in set_well() function (model_cpg.py)
or with higher level “idata” interface:
well_data.add_well(name='PRD', loc_type='ijk', loc_ijk=(1, 1, -1))
or
well_data.add_well(name='PRD', loc_type='xyz', loc_xyz=(250.0, 500.0, 890.0))
self.reservoir.add_perforation(wname,
cell_index=(I,J,K), # location indices
well_index=perf.well_index, verbose=True)
self.reservoir.add_well(wname)
# the last index value (-1) will not be used since there will be a loop over the reservoir layers (assuming the well is vertical)
# real coordinates for each well connection

## Slide 14: Well controls
Geothermal physics
BHP control
rate control
cyclic rate control (a thermal storage example)

## Slide 15: Simulation parameters
Time stepping and convergence parameters (case_base.py)
redirect_darts_output(os.path.join(out_dir, 'run.log'))
Log
Set number of CPU cores
https://open-darts.gitlab.io/open-DARTS/for_developers/configure_hardware.html

## Slide 16: Running the simulation (main.py)
Create the model:
Run the simulation:
Choose cases to run:
physics
geometry and properties case
well control type

## Slide 17: Well results (time_data)
Contains all timesteps
Contains only report timesteps
Add well result of the current timestep to the report
Timestep loop